## Slide 1
HAPPIEST HEALTH DIGITAL TWIN CHALLENGE 2026
HyperTwin
From isolated home blood-pressure readings to a continuously updated, patient-specific state
Research prototype | synthetic data only | not a diagnostic or treatment tool
Arshin Kazi (arshin.kazi20) | Mody University of Science and Technology
Notes: Open with the problem, not the tool. HyperTwin is a research prototype on synthetic data.

## Slide 2
One home reading is one noisy number
Chart: Systolic BP (mmHg)
| Jul 01 |  |  |  |  |  |  |  | Jul 09 |  |  |  |  |  |  |  | Jul 18 |  |  |  |  |  |  |  | Jul 27 |  |  |  |  |  |  |  | Aug 05 |  |  |  |  |  |  |  | Aug 13
Daily home SBP readings | 133.3 | 133.1 | 134.2 | 119.8 | 139.2 | 131.3 | 140 | 126 | 130.1 | 128.9 | 125.9 | 127 | 128.9 | 139.2 | 123.7 | 127.4 | 134 | 124.9 | 134.7 | 129.2 | 138.3 | 138.3 | 129.7 | 128.8 | 128.8 | 123.1 | 136.2 | 129.9 | 127 | 133.8 | 126.7 | 125 | 134.4 | 126.6 | 128.3 | 128.2 | 130.3 | 122.3 | 132 | 118.1 | 127.6
HyperTwin state estimate | 132 | 132.8 | 133.5 | 131.1 | 132.7 | 132.2 | 134 | 132.9 | 132.3 | 132.4 | 132.2 | 131.5 | 131.7 | 132.7 | 131.5 | 130.6 | 131 | 130.2 | 131 | 131.1 | 132.1 | 132.9 | 132.1 | 131.5 | 131 | 130 | 130.6 | 130.7 | 130.8 | 131.1 | 130.6 | 130 | 130.2 | 129.8 | 129.9 | 129.6 | 129.7 | 129.1 | 129.8 | 128.5 | 128.7
Synthetic patient P090, 41 valid morning readings
Home BP is guideline-endorsed
Out-of-office BP is recommended in major hypertension guidance.
Thresholds are for averages
Guidelines cite 135/85 mmHg for home BP averaged over several days.
The trend is what a clinician needs
Single readings scatter. A state estimate shows where the patient is heading.
Sources: ESH Working Group home BP position paper 2021 (PMC9904446); AAFP summary of ISH guidelines 2021
Notes: Guidelines endorse home BP and cite 135/85 for multi-day averages. The chart is a synthetic patient, not real data.

## Slide 3
The insight
Read history and today's data together, as one evolving state.
Historical EHR
age, BMI, medications, family history, last clinic BP
New observations
home BP, sleep, steps, one day at a time
Patient state
a level and its uncertainty, updated every day
+
=
Notes: A static dashboard shows readings. A twin keeps a state that changes when new data arrives.

## Slide 4
HyperTwin
HyperTwin is a research prototype that updates a patient-specific blood-pressure state from historical health information and home readings to forecast next-morning systolic BP risk.
Inputs
Synthetic EHR, home SBP/DBP, sleep, steps
State
Kalman level and variance per patient
Outputs
Next-morning SBP, P(SBP at or above target), contributions
Notes: Read the sentence slowly. Everything on this slide exists in the code.

## Slide 5
How it works: data flow
1 Synthetic EHR
age, BMI, antihypertensive count, family history, last clinic SBP
2 Home observations
timestamped SBP, DBP, sleep, steps; missing days and implausible values
EHR prior
OLS fit on training patients gives the starting level
3 Quality gate
SBP 70 to 250, DBP below SBP, else the reading is skipped
4 Patient state
Kalman level and variance, plus sleep/steps effect
5 Forecast
next-morning SBP, P(at or above target), contributions
6 Dashboard
replay, add reading, what-if
Matches src/twin.py. Parameters fit on 90 training patients only; each forecast uses data before that day.
Notes: Walk left to right. Missing and implausible readings do not move the state; uncertainty grows instead.

## Slide 6
The clinician view
Forecast and risk
Next-morning SBP, 90% interval, P(at or above 135)
State over time
Twin level with 90% band against valid readings
Data quality
Rejected implausible readings shown as red crosses
Actual dashboard screenshot. Synthetic patient P090, replay day 45.
Notes: This is the real Streamlit app. Controls: patient, replay slider, target, add observation.

## Slide 7
A new reading changes the state
Before
After adding 175/95 mmHg
6%
to
53%
risk of next-morning SBP at or above 135 mmHg
A default 150/90 reading gives 6% to 20%.
Illustrative synthetic demonstration, patient P090 at replay day 45. Not a clinical outcome, and not what any real patient would see.
Notes: Verified in the app: 175/95 gives 6% to 53%. The added reading moves forecast and risk; it is not drawn as a point on the chart.

## Slide 8
What if sleep and activity change?
53% to 21%
forecast 135 to 131 mmHg, with 9.5 h sleep and 10,000 steps planned, after the 175/95 reading
How to read it
Uses the sleep and steps associations the model learned. In this prototype those effects are assumptions built into the synthetic data.
An illustration, not a treatment effect.
Actual dashboard screenshot, What-if scenario tab. Extreme settings chosen to make the effect visible.
Notes: The sliders are planned sleep and planned steps for the next day.

## Slide 9
Does the state beat simple baselines?
MAE (mmHg)
Lower is better
Chart: 
| HyperTwin | 7-day mean | Last reading
MAE (mmHg) | 4.25 | 4.33 | 5.44
AUROC
Higher is better (axis starts at 0.85)
Chart: 
| HyperTwin | 7-day mean | Last reading
AUROC | 0.937 | 0.935 | 0.904
Brier score
Lower is better
Chart: 
| HyperTwin | 7-day mean | Last reading
Brier score | 0.075 | 0.076 | 0.099
Clear gain over the last reading. Small gain over the 7-day mean, not shown to be statistically significant.
Synthetic data. 4,024 predictions, 60 held-out test patients (90 training), one seed, no confidence intervals. Twin uses past data only.
Notes: Be honest: the 7-day mean is nearly as good. Results show agreement with our own generator, not clinical validity.

## Slide 10
What the prototype demonstrates
1
Patient-specific state
Starts from each patient's EHR, then learns from readings
2
Bad data handled
Missing and implausible readings do not move the state
3
Short-horizon forecast
Next-morning SBP with a 90% interval and risk
4
Interpretable output
Forecast split into EHR prior, recent level, sleep, steps
5
What-if simulation
Compare planned sleep and steps on the same patient
No first-of-its-kind claim. Many challenge entries build twins for other conditions.
Notes: Only what is implemented and tested is listed here.

## Slide 11
Safety and limitations
Synthetic data only
No real patient information.
Not clinically validated
Results show agreement with our own generator.
Not a diagnosis or treatment tool
Research prototype.
Proxy target
Guidelines use multi-day averages. We predict a single morning.
Small edge over a 7-day mean
Not shown to be significant. One seed.
Assumed effects
Sleep and steps effects are set in the generator.
Notes: State all of this out loud in the video.

## Slide 12
From readings to a state
A reading says what happened. A patient-specific state says where things are heading.
Validation roadmap
1
Test on licensed real home-BP data
2
Add confidence intervals and calibration checks
3
Forecast sleep and steps instead of assuming them
4
Review usefulness with clinicians
Team
arshin.kazi20
Arshin Kazi
Mody University of Science and Technology
https://github.com/arshinkazi/HyperTwin